## Slide 1
CZQM • CONTROLLER TRAINING
TopSky 2.6
A New User's Walkthrough
Menu items and core functions of the EuroScope plugin — explained one screen at a time.
Based on the official TopSky plugin documentation set
v2.6 • 2026

## Slide 2
TopSky 2.6 | COOPANS Setup B | CZQM
1
What is TopSky?
An ATC-system simulation plugin for EuroScope
TopSky is a plugin for EuroScope that recreates the look and feel of the TopSky ATM system used in real-world ACCs.
Customised aircraft tag items and tag menus
Graphical elements on the radar display
Coordination, conflict probe and safety nets
CPDLC data-link messaging support

## Slide 3
TopSky 2.6 | COOPANS Setup B | CZQM
2
How to read this deck
A guided tour, not a manual replacement
ORIENT
Where things live
Global Menu, radar display, track labels, windows.
DRIVE
How you operate
Left/right click conventions, menu folders, toggles.
COORD
Talk to other sectors
PEL/COPN, XFL/COPX, releases, HOP, ROF, RTI/TIP.
REFER
Where to dig deeper
Section + page references back to the official PDFs.
If a screen is shown — that's what you'll see in the sim. If a menu path is in quotes — that's exactly what you'll click.

## Slide 4
01
SECTION
Orientation
The Global Menu and Air Situation Display

## Slide 5
TopSky 2.6 | COOPANS Setup B | CZQM
3
The Global Menu
Your starting point — across the top of the radar screen
If you don't see this bar, the plugin isn't loaded
16:21:40 | UTC clock — opens Clock Window
Setup | Master configuration menu (covered next)
AMS | Airspace Management — activate / deactivate areas
FData | Flight data tools — flight plan list, predicted traffic
Tools | Operational tools — Notepad, Message In/Out, ATC Msgs
MET | Weather — winds, weather messages, weather radar
[x] | Numeric brackets are configurable client-specific menus
Info / MSG / STS | Information windows, messages, status displays
RR | Radar Ranges (sector/airspace selection)
M000-999 | Mach number / SSR code group selection

## Slide 6
TopSky 2.6 | COOPANS Setup B | CZQM
4
Setup menu
Where you tune what the plugin shows you
ASD (Air Situation Display)
Background brightness, label settings, fonts, vector lengths.
Track Control
Which fields appear on tracks for selected vs. unselected aircraft.
Safety Nets
STCA, MSAW, APW, AIW toggles and inhibition settings.
MTCD / TCT
Conflict detection and tactical controller tools on/off.
CPDLC
Data link callsign filters and message presentation options.
Save / Load
Persist your personal layout — windows, label fields, brightness.
Tip: Save your Setup once you have it tuned — it loads automatically when you next sign on.

## Slide 7
TopSky 2.6 | COOPANS Setup B | CZQM
5
Other Global Menu folders
Each opens a sub-menu of windows and toggles
AMS
Airspace Management
Activate, schedule and deactivate restricted/danger areas. Open the AM window from here.
FData
Flight Data
Flight Plan window, Predicted Traffic, Group SSR code window, departure tools.
Tools
Operational Tools
Notepad, ATC Messages, Message In / Out (coordination), Stack Manager, CARD.
MET
Weather
Weather Messages, Upper Winds, weather radar overlay on the ASD.
Info
Information
Airfield Data, Misc Information, NOTAM list, General Info.
STS
Status displays
Safety Nets Status, TCT Status, MTCD Status, Divergence Detection Status.

## Slide 8
02
SECTION
Air Situation Display
Tracks, the radar picture, and the Radar Menu

## Slide 9
TopSky 2.6 | COOPANS Setup B | CZQM
6
Track presentation on the ASD
Every aircraft is drawn as a track + label
A standard 3-line tag. Each piece of text is clickable.
Click the callsign to open the Callsign menu — the most-used menu in the plugin.
Click any data field (CFL, RFL, AHDG, ASP, etc.) to change just that value.
Right-click in empty space on the ASD to open the Radar Menu.
Drag a track or its leader-line to reposition the label.
Read the doc:
General § 5 Air Situation Display, § 6 Track label menus, Appendix 1 (Label field descriptions).

## Slide 10
TopSky 2.6 | COOPANS Setup B | CZQM
7
The Radar Menu
Right-click on empty space anywhere on the ASD
QDM — bearing/distance from cursor.
SEP — separation tool between two tracks.
Quick Look — temporarily reveal hidden tracks.
Maps… — toggle which sector-file maps are drawn.
Track Control… — choose label fields per state.
View… — saved view positions / zoom presets.
Range / Altitude / SSR / CJI / LAT-LONG — picture filters.
Find Track — search by callsign.
Scale Marker / Direction Finder — display add-ons.
This menu controls the radar picture itself, not individual aircraft.

## Slide 11
TopSky 2.6 | COOPANS Setup B | CZQM
8
Track Control
Decide which fields appear on the tag for each track state
Vector / History / Text — sliders for trail and label thickness.
Five state columns: Co (concerned), Ass (assumed), Red (redundant), No (not concerned), All.
For each label field, tick which states it shows on.
DAPs Fields = Downlinked Aircraft Parameters (selected vs. unselected).
Save your Setup once configured — your label preferences persist.

## Slide 12
03
SECTION
Track Label Menus
What every clickable field on a tag does

## Slide 13
TopSky 2.6 | COOPANS Setup B | CZQM
9
Callsign menu
The single most-used menu in the plugin
Transfer — start hand-off to next sector.
Trf & Release — transfer with a release condition.
Freq — give the aircraft a frequency.
Vector / QDM — show vector / bearing line.
Highlight / S-Highlight — visual emphasis.
Hold — open the Hold menu.
Man Trf — manual transfer to a chosen controller.
Mark — drop a private marker on the track.
FPL — open the Flight Plan window.
End CPDLC / Squawk Ident — direct actions.
CPDLC Free Text — send custom uplink.
Inbound Est / Irregular / Missed App — status.
Weather / On Contact / XCouple — extras.
More ▼ — opens the secondary folder.

## Slide 14
TopSky 2.6 | COOPANS Setup B | CZQM
10
Sequence and Waypoint menus
Quick clicks on the route fields of a tag
Sequence number
Waypoint
Sequence number menu
Used by the Stack Manager — set or remove arrival sequence numbers, build holding patterns.
Waypoint menu
Click any waypoint in the route. Direct-to, insert, delete, or use Probe to coordinate a new entry/exit point with the next sector.

## Slide 15
TopSky 2.6 | COOPANS Setup B | CZQM
11
Level menus — AFL, CFL, RFL
Three different fields, three different menus
AFL — Actual
CFL — Cleared
RFL — Requested
Level field cheat-sheet
AFL — what the radar reports right now.
CFL — what you've cleared the aircraft to.
RFL — what's filed in the flight plan.
Click each to open its own picker.
RFL also offers Mach selection on oceanic.

## Slide 16
TopSky 2.6 | COOPANS Setup B | CZQM
12
Tactical menus — AHDG, ASP, ARC
Headings, speeds, and rates of climb/descent
AHDG — heading
ASP — speed
ARC — rate
AHDG — assign or vector a heading. 'Point' lets you direct-to a fix.
ASP — assign IAS, Mach, or speed restrictions.
ARC — Assigned Rate of Climb/Descent — a rate clearance.
Each menu has a More ▼ folder containing HOP, RTI, TIP for sector coordination.

## Slide 17
TopSky 2.6 | COOPANS Setup B | CZQM
13
Other field menus at a glance
Less-used clickable fields, all on the tag
SSR Code
Assign or change the assigned squawk.
Combined Transfer
Resolve a HOP coordination in one place.
Aerodrome
Departure/destination quick edit.
Time
Estimate/ATD/ATA editing for the FPL.
Departure Seq.
Order departing traffic.
GAP
Insert a separation gap into a sequence.

## Slide 18
04
SECTION
Windows
The pop-up panels you'll keep open at all times

## Slide 19
TopSky 2.6 | COOPANS Setup B | CZQM
14
Recommended always-open windows
If you only open four, open these four
Clock Window
Brightness Control
Message In Window — incoming coordinations
ATC Messages
Clock — UTC reference; click to open larger.
Brightness — drag ASD background up/down without leaving sim.
Message In — every incoming PEL / XFL / HOP arrives here.
ATC Messages — broadcast text traffic on your sector.

## Slide 20
TopSky 2.6 | COOPANS Setup B | CZQM
15
Flight data windows
Open from FData / Tools / Callsign menu
Flight Plan window — full FPL editor
Tour
Top buttons — CRE, MOD, Find, Activate, SAC, Terminate, CNL.
C/S, RTE — callsign and full route editing.
Send / CREAPL / MODAPL — push the FPL to the network.
Bottom row — Strip, INI, OCM Tx, Refresh, Apply, Cancel.
Open via FPL on the Callsign menu, or FData → FPL Selection.

## Slide 21
TopSky 2.6 | COOPANS Setup B | CZQM
16
Route & sequence helpers
Visualise routes, build holds, see conflicts
Complete Route
Stack Manager
CARD — Conflict And Risk Display
When to use
Complete Route — full string and waypoints in time order.
Stack Manager — assemble and re-order arrival sequences.
CARD — surface MTCD-detected conflicts with one row per pair.

## Slide 22
TopSky 2.6 | COOPANS Setup B | CZQM
17
CPDLC windows
Data link messaging — see Data Link doc for full set
Current Message Window
History
Microphone Check
Current — open exchanges, awaiting your action.
History — completed and timed-out messages.
Both filterable by aircraft state.
Free Text and standard uplinks come from the Callsign menu's CPDLC items.
Open the CPDLC Setting Window from Setup to tune callsign filters.

## Slide 23
TopSky 2.6 | COOPANS Setup B | CZQM
18
MET and Info windows
Weather and reference data
Weather Messages
Upper Winds
Airfield Data
Misc Information
Weather Messages — METAR/TAF and SIGMET feed.
Upper Winds — winds aloft summary.
Airfield Data — runway, QNH, transition level.
Misc Info — multipurpose panel for sector-specific data.

## Slide 24
TopSky 2.6 | COOPANS Setup B | CZQM
19
Status windows
Open from STS — show what's enabled and inhibited
Safety Nets & TCT Status
TCT Status
Divergence Detection
Each safety-net (STCA, MSAW, APW, AIW, TCT, BS) has an On/Off toggle here.
Inhibit specific callsigns or SSR codes — useful for VFR trainers.
Inhibition Areas list — geographic exclusions.
If something looks broken, this is the first place to check.

## Slide 25
TopSky 2.6 | COOPANS Setup B | CZQM
20
More windows you'll meet
Different windows for different roles — Tower, Approach, Area, Oceanic
Operations Rate
Predicted Traffic
ATFM
Departure Clearance
Holding List
NAT List (oceanic)
Open them only when you need them — every window adds a refresh-rate cost.

## Slide 26
TopSky 2.6 | COOPANS Setup B | CZQM
21
Airspace Management
Activate, schedule and end restricted areas
Airspace Management — start dates / times by area
Workflow
Open from the AMS folder.
Each row = one airspace block.
Start/End columns drive when it's drawn on the ASD.
Lower / Upper limits in flight levels.
Auto column for scheduled activations.
Apply to commit changes.

## Slide 27
05
SECTION
Lists & Safety Nets
Aircraft lists, shortcuts, and the alerts that watch your sector

## Slide 28
TopSky 2.6 | COOPANS Setup B | CZQM
22
Aircraft lists
Same fields as a tag, in row form
Sector List | All flights currently in your sector.
Load Factor List | Sector loading and complexity metrics.
Resectorisation List | Aircraft affected by a planned re-sec.
ETWR List | Estimates To Way-points (your boundary fixes).
Uncontrolled List 1 / 2 | Tracks not yet assumed by anyone.
Lost List | Tracks gone radar-out.
Traffic Mgmt List 1 / 2 | TMA-style configurable filters.
Holding List | Aircraft in holding patterns.
FAST List | Final Approach Sequencing Tool list.
Most lists let you click a row callsign to open the same menus you'd get on the radar tag.

## Slide 29
TopSky 2.6 | COOPANS Setup B | CZQM
23
Safety nets at a glance
Automatic alerts. Toggle from STS or Setup → Safety Nets.
STCA
Short Term Conflict Alert
Imminent loss of separation between two tracks.
MSAW
Minimum Safe Altitude Warning
Aircraft predicted below MSA.
APW
Area Proximity Warning
Predicted entry into a restricted/danger area.
AIW
Airspace Infringement Warning
Aircraft has entered an area without clearance.
Read the doc: General § 10 Safety Nets.

## Slide 30
TopSky 2.6 | COOPANS Setup B | CZQM
24
Monitoring aids and conflict probe
Tools that watch traffic for you
TCT
Tactical Controller Tool
Solo-tracker tagged display for clearance writing — one aircraft, one screen area.
CLAM
Cleared Level Adherence Mon.
Alerts when an aircraft drifts off its CFL.
RAM
Route Adherence Monitoring
Alerts when an aircraft drifts off its filed/cleared route.
MTCD
Medium Term Conflict Detection
Probes the next ~20 min of flight plans for conflicts.
SAP
Segregated Area Probe
Probes flight plans against active areas (D/R/etc.).
BS
Blind Spot
Highlights tracks the radar coverage doesn't actually see.

## Slide 31
TopSky 2.6 | COOPANS Setup B | CZQM
25
Keyboard shortcuts
A handful you'll use every session
KEY | ACTION
F1 / F2 / … | Open / focus the configured plugin window for that slot.
Hold Shift + Click | Multi-select, or extend an action to multiple tracks.
Ctrl + Click | Modifier on most menu items — alternate behaviours.
Right-click empty ASD | Open the Radar Menu.
Right-click a track | Open the track context menu (varies by setup).
Esc | Close most pop-up menus and message dialogs.
See General § 9 Keyboard shortcuts for the full set — your local profile may add more.

## Slide 32
06
SECTION
Coordination
Talking to the next sector through the plugin

## Slide 33
TopSky 2.6 | COOPANS Setup B | CZQM
26
How coordination works
Two controllers, two label colours
Transferring controller
ABC123 IDA
100 ^ OLDPT
180
Accepting controller
ABC123 IDT
100 ^ OLDPT
180
Coordinations colour-code values you propose (Out) and values proposed to you (In).
Reply by clicking the proposed value and choosing Accept, Refuse or Change.
Always keep the Message In window open — that's where incoming coordinations land.
Some coords (ROF, RTI, TIP) need a TopSky-using counterpart; otherwise fall back to text/voice.

## Slide 34
TopSky 2.6 | COOPANS Setup B | CZQM
27
Levels & points — PEL/COPN and XFL/COPX
The two everyday entry/exit coordinations
PEL / COPN
Planned Entry Level / Entry Point
Click the PEL value → choose new level.
Click COPN value → Waypoint menu → Probe → choose point.
Other side answers Accept / Refuse / Change.
XFL / COPX
Exit Flight Level / Exit Point
Click the XFL value → choose new level.
Click COPX value → Waypoint menu → Probe → choose point.
Watch the colour change confirm your proposal.

## Slide 35
TopSky 2.6 | COOPANS Setup B | CZQM
28
Releases
Granting the next sector freedom to climb / descend / vector
A 'Release' is given by the transferring controller to allow the accepting controller to climb, descend, or change heading before the standard handoff conditions apply.
Released for climb — accepting controller may climb the aircraft early.
Released for descent — same idea, the other way.
Released for turn — heading changes permitted.
Issued via Trf & Release on the Callsign menu, or as part of HOP.
Visible in the label until the transfer completes.

## Slide 36
TopSky 2.6 | COOPANS Setup B | CZQM
29
HOP and ROF
Hand-Over Proposal and Request On Frequency
HOP
Hand-Over Proposal
Sent by transferring controller to propose a transfer.
Send via Callsign → HOP — or AHDG/ASP → More → HOP for a conditional.
Three answers: ROF, Accept, or Combined Transfer.
If the recipient isn't on TopSky, only your label is updated.
ROF
Request On Frequency
Sent by accepting controller — "the aircraft is on my frequency".
Doubles as an answer to HOP.
Send via Callsign → ROF.
Indications: ROF in In/Out colour, removed on Transfer or Trf & Release.

## Slide 37
TopSky 2.6 | COOPANS Setup B | CZQM
30
RTI and TIP
Tactical instruction coordination
Use these when one controller wants the other to apply a heading/speed/rate or arc clearance before the formal handoff.
RTI
Request Tactical Instruction
Initiated by accepting controller. "Please vector / restrict speed before sending."
TIP
Tactical Instruction Proposal
Initiated by transferring controller. "I propose this restriction before the handoff."
Send via AHDG / ASP / ARC → More → RTI or TIP. Answers come back in the Message In window.

## Slide 38
07
SECTION
Operating tips
Performance, common pitfalls, and where to read more

## Slide 39
TopSky 2.6 | COOPANS Setup B | CZQM
31
Performance considerations
Keep refresh rates high while panning and zooming
DO
Display only the maps you actively need.
Set ASD background brightness to 100% if it lags.
Close windows you aren't currently using.
Filter Track Control labels by state — fewer fields = smoother panning.
AVOID
Leaving the Weather Map on at low altitudes when not needed.
Loading every active area when only a few apply.
Running with all Safety Nets and CARD open on a low-end machine.
Editing settings mid-session — restart EuroScope after big changes.
Read the doc: General § 3 Performance considerations.

## Slide 40
TopSky 2.6 | COOPANS Setup B | CZQM
32
Common pitfalls for new users
If something looks wrong, start here
No Global Menu visible
Plugin not loaded, or Setup A active. Check COOPANS=1 in plugin settings.
Coordination greyed out in menu
Conditions not met — try again, or use text/voice as a fallback.
Track has no label fields
Open Track Control and tick fields against the right state column.
Safety Net not firing
Check Safety Nets Status — it may be inhibited for callsign or area.
CPDLC items disabled
Aircraft may not be CPDLC-equipped; check FPL equipment fields.
Setup keeps resetting
You haven't saved it — Save in Setup once you have it tuned.

## Slide 41
TopSky 2.6 | COOPANS Setup B | CZQM
33
Where to read more
Three documents in your TopSky 2.6 manual set
GENERAL
General Information (B)
132 pages
Full reference for menus, windows, lists, safety nets, monitoring aids, label fields, colour values.
COORD
Coordination (B)
9 pages
Detailed walkthrough of PEL/COPN, XFL/COPX, releases, HOP, ROF, RTI/TIP.
DATALINK
Data Link Functions (B)
10 pages
CPDLC logon, ADS-C contracts, free-text uplinks, message lifecycle.

## Slide 42
That's the tour.
Open EuroScope, load TopSky, click around — that's where it all clicks.
Questions, additions, or corrections — bring them to the CZQM training team.
CZQM • Controller Training • TopSky 2.6 (COOPANS Setup B)